## Slide 1
2. No Special Storage
Conditions
Archiving:

## Slide 2
3. Last ≥100 Years
Archiving:

## Slide 3
4. No Power Required
(to preserve it)
Archiving:

## Slide 4
5. Easily Transported
Archiving:

## Slide 5
Today’s Technology Options:
Flash
Optical Discs
Hard-Disk Drives
Magnetic Tape

## Slide 6: State of (Digital) Storage Permanence
Magnetic core (early days): permanent (>200 years)
SRAM, DRAM: milliseconds
HDDs: 3-7 years
Magnetic tape: 20-30 years (advertised); 5-7 years in practice
Flash memory (Solid-State Drives): 8-10 years
Optical discs: Recordables ≈ 20 years (advertised); 3-5 years in practice
Archival recordable optical discs (except for M-Disc): 100 years advertised; 5-10 years in practice
  “Optical Disc Life Expectancy: A Field Report (ISOM/ODS 2011, Lihue, Kauai, Hawaii)
M-Disc: DVD >1000 years; BD >300 years

## Slide 7: “Optical Disc Life Expectancy: A Field Report (ISOM/ODS 2011, Lihue, Kauai, Hawaii)
Barry M. Lunt, Matthew R. Linford, Douglas Hansen
Holdings of two libraries – noncirculating discs
Library 1: 8,500 DVDs, 8 brands, standard & archival
Library 2: 18,000 CDs, all archival
Findings:
  ≈2% loss/year (permanent data loss)
  Significant increase in BLER and PIESum8 in all discs (some far beyond spec)